# Text boxes

YES

NO

YES

NO

NO COMMENTS

COMMENTS

- REVISE TO INCORPORATE IF IN AGREEMENT

- DISCUSS TO REMOVE IF NOT IN AGREEMENT

REQUIREMENT

e.g. UTILITY

MECHANICAL

PROCESS DESIGN BASIS

ISSUED FOR COMMENTS (IFC)

ANY ONE OR MORE OF THE FOLLOWING

- TENDER DOCUMENT INCLUDING PROCESS DETAILS

- OVERALL PROCESS DESCRIPTION / DIAGRAM INCLUDING PLANT / UNIT CAPACITY

- LICENSOR PROCESS DETAILS      4. CONCEPT OR PRE-FEED REPORT

AVAILABLE - START

FIRE, SMOKE & GAS DETECTION

ISOLATION, DRAIN PHILOSOPHY

CODES & STANDARDS

e.g. CHANGED SOW,

PROJECTS

e.g. CONTROL & SAFEGUARGING

C & A

COMMENTS

PIPING / PIPELINE

- BACK CHECK

- “SDC”

CHECK AGAINST DISICIPLINE CHECK LIST & CORRECT IF NECESSARY

ISSUE TO CLIENT AS

“ISSUED FOR COMMENTS” (IFC)

COMMENTS

ISSUED FOR “IDC” IN FOLLOWING SEQUENCE

- PIPING

- C&A

- MECHANICAL

- ELECTRICAL

- CIVIL

- PIPELINE (IF APPLICABLE)

- PROJECTS

REVISE TO INCORPORATE

- BACK CHECK

- SDC

GENERATE WORD DOCUMENT. PROCESS DESIGN BASIS MAY INCLUDE BASIS FOR BUT NOT BE LIMITED TO:

- DESIGN PRESSURE

- DESIGN TEMPERATURE

- DESIGN OR MAXIMUM VELOCITIES FOR PIPING / PIPELINES

- NPSHA (PUMP HYDRAULICS)

- FOULING FACTORS (HEAT EXCHANGERS)

- NOZZLE MOMENTUM VALUES (VESSELS / SEPARATORS)

- PIPING ROUGHNESS VALUES

- OPERATION, CONTROL & SAFEGUARDING PHILOSOPHY

- ISOLATION PHILOSOPHY

- DRAIN PHILOSOPHY

- MATERIAL & CORROSION PHILOSOPHY

- UTILITY REQUIREMENT & BATTERY LIMIT CONDITIONS FOR ISBL

- CHEMICAL DOSING REQUIREMENT

- FIRE, SMOKE & GAS DETECTION PHILOSOPHY

- INSULATION REQUIREMENT

ADOPT STANDARD FORMAT WITH FOLLOWING HEADINGS

- ABBREVIATIONS & DEFINITIONS

- INTRODUCTION

- PROCESS DESCRIPTION

- PROJECT SCOPE

- DESIGN

- DESIGN PHILOSOPHY

- DESIGN CRITERIA

- CODES & STANDARDS

- REFERENCES

- LIST OF HOLDS

- APPENDICES

IS STANDARD FORMAT AVAILABLE

e.g. MOC, INSULATION,

COMMENTS

CLIENT

NO

REVISE TO INCORPORATE

YES

ISSUE TO CLIENT AS “APPROVED FOR DESIGN” (AFD)

NO

YES

PREPARE DISCIPLINE CHECKLIST WITH “AFD” REVISION

- INCORPORATED & REVISE IF IN AGREEMENT

- DISCUSS TO REMOVE IF NOT IN AGREEMENT

ISSUED FOR “IDC” IN FOLLOWING SEQUENCE

- PIPING

- C&A

- MECHANICAL

- ELECTRICAL

- CIVIL

- PIPELINE (IF APPLICABLE)

- PROJECTS

COMMENTS

REVISE TO INCORPORATE

PROCESS DESIGN BASIS

APPROVED FOR DESIGN (AFD)

“IFC” – MASTER COPY - AVAILABLE

START